Delmarva Pole Building Supply, Inc.

317 N. Layton Avenue

Wyoming, DE. 19934

Phone # 302-698-3636

Fax # 302-698-5036		February 6, 2011

| BILLING ADDRESS: | BUILDING SITE: |
| --- | --- |
| Mr. Alan Bradley | Mr. Alan Bradley |
| . |  |

Contract to furnish the materials and perform the labor necessary for the completion of a 60’ x 120’ x 16’

Post Frame Building.

Specifications:

- Posts- 		3-Ply 2 x 6 Glue Lam, spaced  8’ on center

- Carriers- 	2 x 12 and/or LVL’s

- Skirtboard-	2 x 8, pressure treated

- Purlins- 	2 x 4, spaced on 2’ centers

- Side Girts-	2 x 4, spaced on 2’ centers

- Trusses-	Engineered to be spaced on 4’ centers, 4/12 pitch

- Roofing/Siding -	29 Ga., 40 Yr. Limited Warranty, CCG Metal

- Footers-		3500 PSI Concrete/Sakrete

- Overhang-	12” Overhang with Vinyl Soffit & Painted Steel Fascia on Eaves & Gables

- Doors-		(A) One (1) 12’ x 14’ Commercial Overhead Door(s)

      - Insulated

(B) One (1) 3’0” x 6’8” Therma-Tru Entry Door

- Fiberglass with Composite Frame

- Lock Set

- 9-Lite

- Windows-	Two (2) 3’0”x 4’0” Vinyl Single Hung Window(s)

      - Double Pane Insulated Glass

      - Interior Grids

      - Screen included

- Gutters-	5” Seamless Gutters with Twelve (12) Downspouts

- Post Protectors-	None Per Customer Request

- Insulation-	¼” Double Bubble under roof steel

- Permit-		Permit to be pulled by DPBS, permit fee to be invoiced separately.

If more than One (1) Permit is required by your jurisdiction you will be assessed an additional

fee for obtaining extra(s) Permit(s)

- Excavation-	Excavation is limited to footprint of building only. Exterior landscaping (Leveling, seeding,

soil stabilization, etc.) is the responsibility of the customer. No swale will be installed around

building. If site is found to be more than 12” out of level, additional charges may apply.

Cost of fill not included and will be invoiced separately. Additional dirt (fill or topsoil) will

not be removed by DPBS, customer is responsible to dispose of remaining soil.

- Concrete-	3500 PSI, Poly Barrier, Fiber Reinforced

      - 4”x 60’x 120’ Pad

      - Two (2) 4”x 3’x 14’ Aprons

      - 4”x 4’x 4’ Service Pad

- Drawings-	CAD Drawings Provided

- Limited to Post Layout, Cross Section Detail, and Elevations

- All necessary drawings to obtain permit

- Silt Fence-	If required by county or local jurisdiction, Customer has the option to provide and install silt 		fence or have DPBS supply and install. The cost of the fence with installation is NOT included 		and will be invoiced separately. Removal & disposal of silt fence not included.

- Debris Removal- Any left over debris/materials are the sole property of DPBS and will be disposed of by

DPBS upon completion of project.

Agreement

The UNDERSIGNED, hereinafter called the Purchaser(s), request the Seller, hereinafter called the Corporation, to construct (a) building(s) in accordance with the specifications which Purchaser(s) hereby approve and for which Purchaser(s) agree to pay THE TOTAL CASH PRICE in accordance with the terms shown below.  The Corporation agrees to perform its part of the contract within a reasonable time after acceptance, subject to delay caused by accidents or conditions beyond its control.  It is also understood that time is not of the essence, as it pertains to this contract, unless noted in writing and signed by an officer of the Corporation.  It is agreed that any delay in commencement of construction in excess of sixty days from the date of the Purchaser’s signature hereto, through no fault of the Corporation, shall be grounds for modification of the price, at the Corporation’s option.  It is expressly agreed that no statement, arrangement or understanding, oral or written, expressed or implied, not contained herein will be recognized.  Purchaser(s) agrees to be responsible for determining the location of the building with the placement of a stake in each corner of the building.  Purchaser(s) is responsible that said location is not in conflict with any building code or zoning ordinance for the proposed location of the building.  Purchaser(s) will obtain and pay for any building permits or sealed drawings needed, and failure to do so will not excuse Purchaser’s performance hereunder.  Purchaser(s) is responsible for the breaking, cutting or damaging of any wires, cables, septic tanks, pipes, etc., in the course of drilling holes.  Purchaser(s) agrees to pay extra costs should surface or underground obstructions such as asphalt, concrete, debris, frost, rocks, water, etc. cause the Corporation to incur extra costs in the course of drilling holes. Purchaser agrees to pay any additional costs caused by changes or additions to the contract terms ordered by an engineer, architect or building inspector. Purchaser(s) is responsible for any leveling, grading, and filling of building site unless otherwise stated in the contract.  Corporation policy will be to set skirtboard at the high point of the building perimeter, plus or minus two inches.  An additional charge will be rendered if low point of grade exceeds twelve inches.  Sliding door height and width may vary from above specifications depending on location.  Purchaser(s) agrees to insure the building and the building materials against fire, acts of God, theft and vandalism immediately upon delivery of any building materials to protect the Corporation against loss or damage until building is complete and paid in full.  Minor work and adjustments shall not be grounds for delaying payment beyond agreed dates.  Purchaser(s) assumes responsibility for damages and consequences, which result from inadequate soil bearing.  All warranties are contingent upon payment in full, according to contract terms.  Purchaser(s) will pay by either personal or business check or cashier check or money order made payable to Delmarva Pole Building Supply, Inc.  DO NOT pay by cash, singularly endorsed cashier’s check or money orders. Purchaser(s) agrees to pay all collection costs and/or reasonable attorney fees.

This agreement will not be binding on the Corporation until counter-signed by an officer of Delmarva Pole Building Supply, Inc. Down payment due upon signing. This contract is null and void if not signed within 30 days of above date.

I have read and understand the above agreement _________ Initials

TERMS:

| Down Payment |  |  | $20,744.73 |
| --- | --- | --- | --- |
| Initial Delivery Of Lumber |  |  | $24,893.67 |
| Upon Installation on trusses |  |  | $29,042.62 |
| On Completion |  |  | $8,297.89 |
| Total Contract Price |  |  | $82,978.91 |

ADDITIONAL OPTIONS: (Not included in above purchase price)

1. Liner Panel-	29Ga., G40 Interior Grade Finish to be installed on Ceiling		$8,769.23

29Ga., G40 Interior Grade Finish to be installed on Walls		$7,015.38

2. Access Opening-	36” x 36” Access Opening with Liner Panel				$78.67

3. Insulation-	R-30 Blown Insulation under truss					$3,138.46

R-19 Fiberglass Batt Insulation on Sides				$2,953.85

4. Insulation- 	R-Board on Ceiling of Building					$9,692.31

R-Board on Side Walls of Building				$7,384.62

5. Interior Girts-	2” x 4”s  2’ on center on Ceiling					$2,953.85

2” x 4”s  2’ on center on Side Walls				$2,584.62

The above specifications and agreement, and the terms above are satisfactory and are hereby accepted.  The Corporation is authorized to furnish the materials as specified.  Payments will be made as specified above under TERMS.

Purchaser ________________________________________________ Date ____________

Sales Person ______________________________________________ Date ____________

Officer_____________________________________________________Date____________